Currently, the only feasible technology for mirrors of the 30 meters class is segmentation. The stiffness is supplied by a control system using actuators for the rigid-body movements of the segments and edge sensors measuring, at high rate, the relative heights of adjacent segments. The edge sensors need to be calibrated by optical sensors measuring the relative heights, from now on called piston steps, between neighboring segments.
On the one hand, the sensor must be capable of measuring large piston steps of several micrometers after installations of segments. On the other hand, preferably also during operations to continually check the performance of the edge sensors, the sensor should be capable of measuring small piston steps of a few nanometers.
This paper compares two sensors that use spatial filtering in the focal plane to convert the phase steps into intensity variations. One of them is a simple circular pinhole and the other one a circular phase mask, that is a special type of a phase contrast sensor [?]. The phrase mask diameter will be used for the diameter of the pinhole as well as for the diameter of the central circular part of the phase contrast generating the phase delay.
The theoretical comparison is based on a single phase step in the middle of a circular aperture and assumes that segments are not tilted with respect to each other.
In the case of the pinhole the spatial filtering in the focal plane blurs the wavefront in the entrance pupil. This leads to an overlap and therefore interference between the initially separated areas of the two segments. The blurring will only have an effect for regions with variations in the initial complex amplitude. For the wavefront studied in this paper, this is close to the location of the piston step. For large pinhole diameters, the blurring extends over only a small region, which leads to a modification of the signal only close to the location of the phase step, therefore generating a well localized signal. Phase differences will then generate partial destructive interference, resulting in a reduced intensity at the location of the step.

 In the propagation to tIn the phase contrast sensor, the expected effect is the filtering of the low order aberration. This is the result of a combined effect of the phase mask: the center part of the focal plan is delayed and reemitted in a quasi-spherical wave.he pupil plan, this focal plan center part interfere with the outer part.

Tests with the phase contrast sensor have been done in the laboratory and on sky with the APE experiment [?]. The spatial filter in the Zernike phase contrast Unit Sensor (ZEUS) was a parallel plate with a circular dip in the middle. The center of the dip was aligned in the focal plan with optical axis of the telescope. The depth of dip was equivalent to a phase shift of a quarter of the central wavelength of the chosen bandwidth. The piston steps were extracted from the signal by a fit of a theoretically expected shape.
For both sensors, a relatively coarse phasing can be done by modulating the piston step within a large range of several wavelengths and detecting the maximum of the coherence envelope of the signal. For small piston steps, one can do single measurements with a narrow bandwidth, if sufficient light is available, or a broad bandwidth, if only dim stars are available.
The comparison between the two sensors in Section 3 will be done without and with taking into account atmospheric effects. Section 4 will discuss the optimal choice of the sampling for a possible use of this type of sensor in the ELT.
The comparison will be based on the content of information in the signals analyzed by specific algorithms. The chosen type of information is the Fisher information because of its close relationship to the achievable precision of the measurement expressed as the rms of the measurement error.
# The Fisher information and the Cramer Rao Lower bound
This application of the Fisher information to phase measurements has been discussed in [Noethe..] and [Surdej.]. This section only summarizes the essential features of the Fisher information.
The Fisher information can be defined by
I left (θ right ) =4 int from {-∞} to {+∞} {{left ({∂ sqrt {p left (x mline θ right )}} over {∂θ} right )} ^ {2} dx} ,
where p left (x mline θ right ) is the probability that a photon will be detected at the location x on the detector in the exit pupil, if the relative piston step is θ . Furthermore, the integral of p(x|θ) $p(x|\theta)$ over the pupil is equal to 1, expressing that the definition is valid for a single photon. The Fisher information is related to the lower bound (Cramer-Rao bound) with which the parameter θ can be estimated from the signal p(x|θ) . For a number {N} rsub {photon} of detected photons the Cramer-Rao bound (CR) is given by
{σ} rsub {CR} ≥ {1} over {sqrt {I left (θ right ) {N} rsub {photon}}} (1) $\sigma_{\mathrm{CR}} = ...$
For the measurement of a piston step θ the fundamental limit is then given by [?]
{σ} rsub {CR} = {λ} over {2π sqrt {{N} rsub {photon}}} (2)
All calculations will be done for one photon and the normalized Fisher information and the Cramer-Rao bound will be defined by
widetilde {I} =I {λ} over {2π} \tilde{I} =\sqrt{I} \frac{\lambda}{2\pi}
{widetilde {σ}} rsub {CR} = {σ} rsub {CR} {λ} over {2π}
     $\tilde{\sigma}_{{\textrm CR}} = \sigma_{{\textrm CR}} \frac{2\pi}{\lambda}
The fundamental limit for both widetilde {I} and {widetilde {σ}} rsub {CR} will then be equal to 1.
# Comparison between ideal pin hole and phase contrast
For the discussion of the performance of the two sensors related to the measurement of phase step we will consider parameters that are suitable for measurements on a 40 m class telescope. To obtain the maximum of information, the optimum diameter size of the phase mask is approximately 1.5 times the diameter of the PSF [Isabelle]. In normalized parameters this translates to $\tilde{w}_{\mathrm m,opt} \approx 1.5/\tilde{r}_{0}$. If the seeing is improved in the EELT by the adaptive M4, one may expect Fried parameter of the order of $r_{0}\approx 400\,\mathrm{mm}$. With an aperture radius of 20 m this gives to $r_{0}/a \approx 0.02$ and, consequently, $\tilde{w}_{\mathrm m,opt} \approx 75$.
For the phase contrast sensor the best phase delay by the inner part of the mask is $\lambda/4$ [??]. This phase delay will be used in all calculations.
It is convenient to express the parameters in normalized form. We define the normalized phase step as $\tilde{\theta} = \theta/\lambda$, and, with $a$ being the half-diameter of the entrance pupil and $\lambda$ the wavelength of the light, the normalized radius of the mask as $\tilde{w}_{\textrm{m}}= {w}_{\textrm{m}}2a/\lambda$.
All calculations are done for monochromatic light.
## Signals
For large radii of the mask in units of $\lambda/(2a)$ the value at $x=0$ is approximately $0.5\, \cos^{2}(\theta/\lambda$)$.and Figure 1 shows typical signals for the two sensors without atmospheric disturbances as functions for various phase steps.

Figure 1: Typical signal for various phase step for the pinhole sensor. The black line in the figure on the right hand side is the superposition of lines for $\theta/\lambda=0.0$ and $\theta/\lambda=0.5$.
The plots on the left hand side of Fig.?? and Fig.?? are done with $\tilde{w}_{\textrm{m}}=20$ to show that f for both sensors the number of maxima is approximately equal to $\tilde{w}_{\textrm{m}}$. Whereas for small masks with diameters of the order of the Airy disk the signal would be spread over the whole exit pupil, it is well localized for larger masks. For $\tilde{w}_{\textrm{m}}=75$ the side maxima are hardly visible, but the signal at the center is more pronounced.
For large radii of the mask in units of $\lambda/(2a)$ the value at $x=0$ is approximately $0.5\, \cos^{2}(\theta/\lambda$)$.
Without atmospheric disturbances the width Δx of the signal can be defined as the distance between the first zeroes to the two sides of the origin.
The width is then
Δ x left [mm right ] =253,5 {λ[μm]} over {a["]} ,$\Delta x$ for pinhole and phase contrast sensor.

The signal of the pinhole sensor is always symmetric around x=0 . Therefore, the sign of the phase step is not detectable.

Figure 2: Typical signal for various phase step for the phase contrast sensor.

The signal of the phase contrast sensor with a phase delay of the mask of {λ} over {4} is more complex than the one of the pinhole sensor, as shown in Fig.??. in general, it is a superposition of a symmetric and an antisymmetric signal. Because of the asymmetry of the signals, in particular for small phase steps, one can detect the sign of the phase steps.
Fig. ?? shows the intensities for $\tilde{r}_{0}=0.02$ and $\tilde{w}_{\textrm{m}}=75$.

With atmospheric disturbances the width of the signal has been defined in [?] as the distance between the x-coordinates for which the signal drops under 10% of its maximum. For the phase contrast sensor the width is
\Delta x & \approx & 1.23\, \frac{\lambda}
  {2 w_{\mathrm{m}}[1+1.24(\theta_{\mathrm{seeing}}/
        (2w_{\mathrm{m}}))^{2}]^{1/2}}\\
  \Delta \tilde{x} & \approx & 1.23\,
       \frac{1}{\tilde{w}_{\mathrm{m}}}
  \, \Big(1+1.24/(\tilde{r}_{0}\tilde{w}_{\mathrm{m}})^{2}
        \Big)^{-1/2}
Therefore, with the optimum choice of of $\tilde{w}_{\mathrm{m}}$ as $1.5/\tilde{r}_{0}$, the signal width is approximately 30% smaller than the signal with atmospheric disturbances.

## Fisher information

Fig.?? shows for both sensors, no atmospheric disturbances and various phase steps the change of intensities due to a change of the normalized phase step of 0.01 and Fig.?? the corresponding Fisher information densities.
Apparently, for the pinhole sensor, the Fisher information densities are zero for $\tilde{\theta}=0$ and $\tilde{\theta}=0.5$. This is in line with the pdf at x=0 being equal to $0.5\, \cos^{2}(\theta/\lambda$. Contrary, the Fisher information densities of the phase contrast sensor are of the same order of magnitude for all
phase steps.

Figure 3: Change of intensities due to a change of the normalized phase step of 0.01.

Figure 4: Fisher information densities for various normalized phase steps and no atmospheric disturbances.
Fig.?? shows the Fisher information densities for $\tilde{r}_{0}=0.02. Qualitatively, they are rather similar to the ones with atmospheric disturbances. However, the values are about 50% smaller.

Figure 5: Fisher information densities for various normalized phase steps and $\tilde{r}_{0}=0.02$.
Figure 6 shows, for both sensors, the square root $\tilde{I}$ of the normalized Fisher information as a function of the piston step, $\tilde{w}_{\mathrm m} \approx 75$, without atmospheric disturbance and with a seeing of $\tilde{r}_{0}=0.02$. As already mentioned above, themajor difference between the two sensors is that the phase contrast sensor is sensitive, although with significant variations, for all piston steps, whereas the sensitivity of the pinhole sensor converges to 0 for $\theta \rightarrow 0$ and $\theta \rightarrow \lambda/4$ . Surprisingly, for piston steps around ~0.27 $\lambda$, the pinhole sensor is more sensitive than the phase contrast sensor.

Figure 6: Normalized sqaure root of the Fisher information for both sensors, without and with atmospheric disturbances.
Qualitatively, for both sensors, the dependence of $\tilde{I}$ on the phase step is rather independent of the seeing conditions. The Fisher information is largely determined by diameter of the mask. A seeing with $r_{0}\approx 400mm$ reduces $\tilde{I}$ only by roughly a factor of 2.
Because of its low sensitivity of the pinhole sensor for small phase steps, the pinhole sensor is probably not suitable for phase measurements with dim stars during operation of the telescope. However, it could still be used for measurements with modulations of the piston step for a coarse phasing after installation.
# Optimal sampling for phasing with phase mask
All the previous result were obtained with simulations using samplings that were at least 100 times better than realistic samplings.
With a working wavelength of 0.65 μm and a pin hole diameter of 1”, the signal width is approximately 165 mm. For a segment size of 1420 mm edge to edge the signal width is approximately 1/10 of a segment.
The sampling will then be defined as the number of pixels across the signal width Δx .
For the 39 meter telescope to be built by ESO. There are 30 segments across the diameter, with a central obstruction equivalent to 9 segments. All 39 segment must to fit inside the camera, while providing sufficient sampling for the signal. In [Yaistskova] the recommendation is to use 4 point across the signal width. This means the detector must have at least a 1600*1600 pixels. In term of the Cramer Rao bound this means that the lowest possible error of the sensor change from 0, 24 λ to 0, 29 λ . This loss can easily be compensated by capturing twice the number of photon.
For the pin hole sensor, using the same sampling, this represent a loss of {3.10} ^ {-3} λ .
Figure 7 shows, for both sensors, the dependence of the Fisher information on the sampling. The pinhole sensor is much less sensitive to an under-sampling. The major reason for this probably is the symmetry of the signal.
It is also interesting, that the pinhole sensor reaches the infinite sampling limit
at a sampling of approximately 10, whereas the Fisher information for the phase contrast sensor does not saturate even with samplings around 40 or more. This behaviour is the same in the presence of atmospheric seeing.

Figure 7:average fisher information across the capture range for different signal sampling.
# Feasibility for phase step measurement in the EELT
The pinhole sensor will, despite its low sensitivity for small phase steps, be feasible for coarse phasing, that is measurement using phase steps over a large range.
For measurements of small phase steps the phase contrast sensor seems to be more promising. This would particularly be true, continuous or frequent measurements during observations were envisaged. In this case only rather dim reference stars would be available, which requires Fisher informations as large as possible.
With a sampling of 4 pixels across the signal width, the square root of the normalized Fisher information would be of the order of 0.004. With a broadband measurement with a bandwidth of 300 nm this might be reduced to 0.002, equivalent to $\sigma_{\textrm CRB}} \approx 500 \lambda/(2\pi) \approx 50 \mu m$.
Reducing this to 25 nm would require total number of photons across the aperture of approximately $4 \cdot 10^{6}$. Assuming that only 20% of the star light reaches the sensor, this could be achieved with a star of magnitude ??, since the light from the whole aperture contributes to the signal.
This estimate is fully in line with measurements on the APE experiment [??], where the ZEUS sensor measured phase steps with errors of ?? nm rms with stars of magnitude ??.